## Slide 1: Extent of O3 Photochemical Production in Indoor Environments
Josh + Josh
2 x Josh
Josh2?
7 December 2017, 3:53 AM… 

## Slide 2
Why Study Indoor Air Chemistry?
We spend ~80-90% of our time indoors
Relative to outdoor chemistry, indoor chemistry is understudied
What are the impacts of indoor chemistry on human health?
What are the sources of primary and secondary pollutants indoors? Surfaces?

## Slide 3
Pollutants Indoors: Processing and Origins
O3
VOC
VOC
O3
SOA
SOA
VOC
SOA
O3
VOCs, O3, and SOA have sources originating from both outdoor and indoor environments and undergo complex chemical processing

## Slide 4
Outside, VOC processing is largely driven via photochemical processes
However, indoors, the light sources can vary—how does this impact photochemical production of secondary pollutants like O3 and SOA?
Photochemistry Indoors vs. Outdoors
Note that CFTs and Sunlight transmitted indoors from outdoors are markedly weaker than outside sunlight
Kwan et al., 2017

## Slide 5
Ozone Indoors vs. Outdoors
O3 is produced via photochemical cycles involving NOx, VOCs, and light  Formed indoors largely in photocopiers, laser printers, etc.
O3 is thought to mainly originate indoors from outdoors

## Slide 6
Main Research Question
To what extent does indoor photochemistry produce and affect O3 relative to the amount transported from outside?

## Slide 7
Factors to be Investigated for O3 Production Indoors
VOC Mixing Ratios
Light Source
[O3]0
Surface Deposition
NOx Mixing Ratios
The F0AM Model provides an excellent tool to model O3 production in this environment—indoors, we are essentially living in a box!
November 24, 2017 from RSC.

## Slide 8
Isoprene – from human breath
Aromatics (toluene, benzene, xylenes) – from paints, solvents, etc.
Limonene/α-pinene – found in air fresheners
HONO – thought to originate from NO2, H2O, light, and a surface
NOx– transport from outside; photolysis of HONO
H2O2  Ozonolysis of alkenes; HO2 self-reaction
O3 initialized to 20 ppb unless stated otherwise
Base Model Inputs: VOCs and Inorganics
Note: Low and high VOC mixing ratios correspond to Limonene at 0.35 ppb and 70 ppb, respectively. All other VOCs are at ~1 ppb or less. Model was run for 1 hour to account for typical air exchange rates

## Slide 9
Light source = Indoor Sunlight from Kowal et al., 2017
Surface Deposition Rate = 5/hr from Weschler et al., 2000
Model Inputs Contd.: Surface Deposition and Light Source

## Slide 10
Base Case Model Run Example (Low VOC)
At first glance, mixing ratios of species are constant except for O3  Warrants Investigation!

## Slide 11
Varying Indoor Light Source
The maximum observed outdoors is likely due to elevated photon flux  Propagating the VOC/NOx/O3 cycle
Indoors, decreases in [O3] are likely a result of lower photon flux  Does NO2 efficiently photolyze here?

## Slide 12
Photon Fluxes and NO2: Photolysis Efficiency Indoors
Indoor photon fluxes at wavelengths < 390 nm are small indoors relative to outdoors  less NO2 photolysis, leading to reduced O3 production

## Slide 13
Varying Initial [O3] at Indoor Sunlight
2 O3 regimes observed: one where O3 is initially produced and one where O3 decays  Null Cycle Equilibria (NO2/O3)
For Low VOC, O3 profiles decrease over time due to lack of RO2 being produced; vice-versa for High VOC
-Note: We looked at plot rates and saw the RO2 species were produced when O3 started to increase for high VOC

## Slide 14
Varying Surface Deposition
Increasing surface deposition rate results in significant loss of O3 (almost 100% loss over an hour)  strong sink!
High VOC case without surface deposition shows a small decrease due to NO + O3; increase again due to RO2

## Slide 15
Varying [NOx]
At NOx = 0 ppb for both VOC regimes, loss of O3 is completely dominated by surface deposition
For Low VOC (VOC limited): <1500 s, O3 decreases fast due to NO + O3; >1500s, slower removal due to NOx cycling
For High VOC (NOx limited): O3 is more sensitive to NOx  50 + 100 ppb NOx cases show larger differences compared to low VOC; however, there is always a decrease in O3 independent of NOx mixing ratios

## Slide 16
Base Case Model Run Example (Low VOC) : Revisited
1) Low photon fluxes <390 nm  less NO2 photolysis  less VOC/NOx/O3 cycling
2) High (~20 ppb) O3 mixing ratio leads to a sharp decrease due to null cycle equilibria and lack of RO2
3) Modest deposition rate (5/hr) is strong enough to cause O3 to sharply decrease and doesn’t go to 0 due to null cycle equilibria
4) NOX mixing ratios result in a non zero ozone mixing ratio

## Slide 17
Conclusions/Future Directions
1) Photochemistry appears to be relatively weak indoors with respect to O3 production
2) Surface Deposition Rates appear to be significant in O3 removal and should be taken into account in all indoor air chemistry models (What about other species?? This is not currently known!!)  Surfaces extremely important!
3) Indoor Field Campaign: Measure VOCs + HCHO/CHOCHO  F0AM  Constrain/Compare
4) Measurement of Deposition and Resuspension Rates of Indoor VOCs/Inorganics